## Slide 1
pyckt
Python re-implementation of the acst analog-circuit-synthesis tool
Progress report · Firas · 2026-06-05
pyckt (Python): github.com/cda-tum/pyckt
acst (C++ reference): github.com/inga000/acst

## Slide 2
Goal & approach
• Translate acst (~112,000 lines of C++) into a maintainable Python package
  – acst = analog circuit synthesis tool from TU München
• Reproduce the same six analysis modes …
  – structrec · partitioning · rulegen · automaticsizing · synthesis · toplibgen
• … and the same outputs, so Python can be validated against the original
  – acst is the reference: for any input, pyckt should match it
• Validation enabler: pyckt emits output in acst's exact XML schema
  – (--output-format acst) → outputs diffed tag-for-tag, not by eye

## Slide 3
Status at a glance
All six modes run end-to-end
Mode | Pipeline | Output vs acst | State
structrec | yes | 16/16 devices + full hierarchy match | Done
partitioning | yes | 19/19 devices in same section | Done
rulegen | yes | 10/10 items, 9/10 same level | Done
automaticsizing | yes | schema + perf models match; W/L tuning open | Functional
synthesis | yes | 4,914 candidates ranked; netlists = placeholders | Framework
toplibgen | yes | 1,725 topologies enumerated; netlists = placeholders | Framework

## Slide 4
Validation: recognition modes match acst
Deterministic modes — exact agreement
• structrec — structure recognition
  – 16/16 devices to same structure; full composite hierarchy identical
  – fixed this period: spurious LevelShifter + swapped diff-pair pins
• partitioning — circuit partitioning
  – 19/19 devices in same section (gm-path stages / bias / load / caps)
  – was the biggest gap (1/6) → re-implemented to acst's stage logic → 19/19
• rulegen — sizing-rule library
  – same pairLibrary artifact; 10/10 items, 9/10 at same hierarchy level
→ See side-by-side XML in samples/structrec, samples/partitioning, samples/rulegen

## Slide 5
Validation: automatic sizing
Output format & models match; optimiser tuning open
• Output schema matches acst
  – ExpectedPerformance / Currents / Dimensions
• Performance models implemented
  – Ft, slew rate, phase margin (were stubbed → 0)
• Produces a valid sized HSPICE netlist
  – samples/sizing/sized_netlist_pyckt.hspice
• Open: solver under-sizes the design
  – not yet at acst's operating point — main numeric item
Metric | acst | pyckt | Δ
Gain (dB) | 90.0 | 91.3 | 1.4%
Slew (V/µs) | 22.5 | 24.5 | 8.8%
Power (mW) | 6.12 | 7.53 | 23%
Phase margin | 60.7 | 87.2 | ✗
Transit f (MHz) | 6.93 | 23.1 | ✗
Area (µm²) | 10868 | 207 | ✗

## Slide 6
Synthesis & topology generation
Enumeration + ranking framework complete
• synthesis — enumerate, size, rank candidate topologies
  – 4,914 candidates ranked (rank / score / gain / power / area / Ft)
  – samples/synthesis/synthesis_ranking_pyckt.json
• toplibgen — enumerate the op-amp topology library
  – 1,725 topologies (133 one-stage + 1,592 two-stage), each with metadata
• Framework done; per-topology netlist bodies still placeholders (next phase)
• acst's generators run minutes–hours → direct output diff deferred until offline run

## Slide 7
Recent progress & next steps
• Done this period
  – acst-compatible output writer (all modes)
  – partitioning re-implemented → 1/6 → 19/19
  – structrec hierarchy + pin-label fixes → 16/16
  – sizing performance models implemented
  – parser robustness fixes
• Next
  – tune sizing solver to acst's operating point
  – real synthesis / toplibgen netlist bodies
  – reconcile rulegen level + persistence
  – derive partitioning nets from structure tree
  – run acst to completion → validate synth/toplibgen